## Slide 1: Mstar eCos application
Jerry-HT Hsieh
2013.12.16

## Slide 2: Agenda
Tool chain and Source tree
Program the boot loader (MBoot)
Build the application
Run the application
  From USB flash disk
  From SPI without Mboot
  From SPI with MBoot

## Slide 3: Tool chain and Source tree (1/2)
Build Server Path
  >>export PATH = /tools/mipsisa-3.4.4/bin:$PATH
Sync Code Path
//THEALE/Uranus/Keltic/DDI_Package/ddi_pkg_ecos/
//THEALE/Uranus/DDI_MISC/

## Slide 4: Tool chain and Source tree (2/2)
Source Tree
  boot : boot loader dependence source code
  bsp
    Include : utopia header file
    lib : utopia library
  cus_mstar : DDI main source code
  ecos : ecos kernel library
  verify : verify command sample script

## Slide 5: Board Configurations
Build options (cus_mstar/project/mstar_demo/config)
Select correct board option
Select correct chip part name

## Slide 6: Build the application  make
cd ../ddi_pkg_ecos/cus_mstar/project/mstar_demo
Edit the file “config”
  Select the CFG_BOARD and CFG_DVB_TYPE
make clean;make
Application  bin/keltic_ecos.bin
Packed Application and Boot Code 
  DDI_Package\ddi_pkg_ecos\boot\mboot\out\flash.bin

## Slide 7: 1. Start to flash Boot Code to SPI
Config

## Slide 8: 2. Load Binary with ISP TOOL
Read Correct Mboot binary

## Slide 9: 2. Flash Binary to SPI with ISP TOOL
Click run to flash binary to SPI

## Slide 10: 1. Run the application from USB
10
If connect or write flash fail, please perform the following steps
  Press down the “Enter” while booting
  Execute the command “du”
    << MStar >># du
  Un-Check the Re-Connect check box in ISP tool
  Repeat the procedure again (1~5)

## Slide 11: 1. Run the application from USB
11
Execute the following command in the boot loader
  << MStar >># setenv bootcmd ‘usb start ; fatload usb 0 0x80000180 keltic_ecos.bin; go 0x80000224
  << MStar >># saveenv
Copy the bin/keltic_ecos.bin to USB disk and plug to the board
Reset the board

## Slide 12: 2. Run the app+sboot from SPI
Flash image
  …/ddi_pkg_ecos/boot/sboot/flash_with_ecos.bin
  This will Run the app with Sboot

## Slide 13: 2. Run the app + mboot from SPI
Flash image only first time
  …/ddi_pkg_ecos/boot/mboot/out/flash.bin
  This will Run the app with mboot

## Slide 14: 2. Run the app + mboot from SPI
  After first time flash.bin already booting to DDI
  We can just place the flash.bin to USB directly and reboot for auto updating FW

## Slide 15: Add verify/demo code (1/3)
../cus_mstar /app/demo/appDemo.c
Command
Function
Input Mask

## Slide 16: Add verify/demo code (2/3)
Input Mask
  1: input string(MS_U8*), 0: input (MS_U16*);
These argument are string type

## Slide 17: Add verify/demo code (3/3)
Ex : Help Function
>> help

## Slide 18: Q & A